## Slide 1: Micro Plate Rounds
Mycology
Session 13

## Slide 2: QuantiFERON
Harada, 2008
≥ 0.35 IU/Ml cut-off established by manufacturer to give “best” combination of sensitivity and specificity based on ROC curve analysis (population derived cut-off)
Small changes in level of response may be expected on individual level (inherent variability of test, lab artifact, variability of individual immune response over time)
  If serial testing is discordant, dx/tx dependent on clinical & historical information
Depending on prevalence & risk of MTB screening situation, different cut – offs may be used to optimize sensitivity or specificity

## Slide 3
Comprehensive Review of Infectious Diseases, 2020

## Slide 4: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture |  | 
Anaerobic culture |  | 
AFB culture |  | 
Fungal culture |  | 

## Slide 5: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | 
Anaerobic culture |  | 
AFB culture |  | 
Fungal culture |  | 

## Slide 6: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture |  | 
AFB culture |  | 
Fungal culture |  | 

## Slide 7: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | 
AFB culture |  | 
Fungal culture |  | 

## Slide 8: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | No
AFB culture |  | 
Fungal culture |  | 

## Slide 9: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | No
AFB culture | No | 
Fungal culture |  | 

## Slide 10: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | No
AFB culture | No | Yes
Fungal culture |  | 

## Slide 11: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | No
AFB culture | No | Yes
Fungal culture | No | 

## Slide 12: Poll #1
Although actual tissue, aspirates, and fluids are specimens of choice over swabs, which specimen containers/devices can be used for each of the following cultures?
 | Eswabs | Sterile Cup
Aerobic culture | Yes | Yes
Anaerobic culture | Yes | No
AFB culture | No | Yes
Fungal culture | No* | Yes
Can share sterile cup if needed
≥ 10 mL of fluid preferred for fungal/AFB culture (2 mL for CSF)
Notes:   One piece of tissue/swab in one Eswab container can be submitted for both aerobic and anaerobic cultures

## Slide 13: Specimen Collection
Biopsy, aspirate, currettings from advancing border of lesion are essential to demonstrate invasive fungal disease
Use swabs only for superficial skin or mucous membranes infections

## Slide 14: Specimen Processing
1. Process promptly – within 2 hours of collection
If unable to process promptly, refrigerate
  Exceptions:
    Bone marrow → room temp
    Blood cultures → room temp
    Mucorales or Dermatophytes suspected → room temp
Fungal tissue cultures are minced, rather than grinded
  Zygomycetes have few septations → grinding between septations can kill pieces of hyphae

## Slide 15: Specimen Processing
1. Process promptly – within 2 hours of collection
2. Direct Smear
Visualization of fungal elements to give early evidence of fungal infection [e.g. size of yeast, type of budding, hyphae (pseudo, true, septations, pigment)]
Can guide selection of appropriate media or growth conditions
Limitations:
  Does not rule out fungal infections (culture must be done)
  Many fungi have similar appearances on direct mounts
Blood or bone marrow → no direct mount done. Collected in yellow top tube with SPS, transferred to Myco-F bottles, incubated in BacTec

## Slide 16: Direct Smear
Wet Mount, KOH-Calcofluor
  KOH:
    Softens, digests, and clears surrounding tissue to make fungal elements more visible
  Calcofluor White:
    Binds to cellulose and chitin → fluoresces when exposed to UV light
    Bacteria may fluoresce to a lesser degree; presence of fungi should be determined based on morphology

## Slide 17: Poll #2
A KOH direct examination of skin scrapings from torso lesions reveals short curved hyphal elements along with round yeast cells in compacted clusters. After visualization of these fungal elements, the Micro Lab will…
A. Add an overlay of olive oil to agar
B. Perform a germ tube test
Use Sabouraud Heart Infusion Agar with blood
as culture media
*Note - At MMC, no KOH-calcofluor performed on skin, hair, nail cultures
Specimens directly inoculated into Mycosel culture bottles by providers

## Slide 18: Poll #2
A KOH direct examination of skin scrapings from torso lesions reveals short curved hyphal elements along with round yeast cells in compacted clusters. After visualization of these fungal elements, the Micro Lab will…
A. Add an overlay of olive oil to agar
B. Perform a germ tube test
Use Sabouraud Heart Infusion Agar with blood
as culture media
Notes: Blood cultures usually negative in absence of lipid-enriched media – communicate clinical suspicion with the micro lab

## Slide 19: Malassezia furfur
“Spaghetti and meatball appearance”
Lipophilic dimorphic fungi
Cannot synthesize medium-long chain fatty acids, requires exogenous supply for growth
  Tend to colonize oily areas of skin
  Contaminates parenteral lipids
Communicate with lab if suspected. Isolation requires media enriched with fatty acids (olive oil or tween to Sabouraud dextrose agar or Dixon’s media)
Clinical:
  Pityriasis versicolor, folliculitis
  Systemic disease. RF: preterm neonates, CVC, parenteral lipids, immunocompromised

## Slide 20: Specimen Processing
1. Process promptly – within 2 hours of collection
2. Direct Smear
3. Media Inoculation and Incubation

## Slide 21: Culture Media
Sabouraud dextrose agar (SAB), Inhibitory Mold Agar (IMA), Sabouraud Heart Infusion Agar (SABHI), Mycosel/Mycobiotic agar (MYCO), among others…
Each culture media has advantages and disadvantages
Media selection for inoculation is based on specimen type, identifying characteristics on direct mount, and clinically suspected fungi/mold
Sporothrix schenckii on SAB
Mycosel/Mycobiotic agar

## Slide 22: Incubation
Incubated at 28 – 30oC for 4 weeks
Examined twice weekly for new growth
To ensure selection of optimal media and incubation conditions, notify lab if particular agent is suspected
    Mucormycosis: Processed stat. Temperature sensitive and does not survive refrigeration
    Dimorphic fungi: SABHI media used. If Histoplasma suspected, BM and liver biopsies are held for 6 rather than 4 weeks

## Slide 23: Specimen Processing
1. Process promptly – within 2 hours of collection
2. Direct Smear
3. Media Inoculation and Incubation
If growth, additional identification methods can be used based on appearance on lactophenol blue, gross colony morphology and growth rate
Yeast → MALDI-ToF, BD-Phoenix
Mold → manual morphologic ID
4. Identification

## Slide 24: Lactophenol Cotton Blue (LPCB)
Used once fungal colonies are growing in culture
Helps identify morphologic structures and characteristics
No role in tissue staining
Cotton blue: Stains chitin on fungal wall
Lactic acid: preserves fungal structures
Phenol: kills any organisms suspended in the stain
Microscopical appearance of Histoplasma capsulatum microconidia and macroconidia on LPCB stain

## Slide 25: Poll #3
The Micro Lab will not routinely identify non-albicans Candida in culture to the species level if the specimen type is a…
BAL specimen
B. Urine specimen
C. Tissue specimen
D. Blood culture

## Slide 26: Poll #3
The Micro Lab will not routinely identify non-albicans Candida in culture to the species level if the specimen type is a…
BAL specimen
Urine specimen
C. Tissue specimen
D. Blood culture
For non sterile sites (urine, sputum/tracheal, wound, genital),
ID of C. albicans
ID of other non C. albicans only performed upon request
*Urine SOP applies (e.g. CFU/mL of organisms, # of organisms, urine specimen type)

## Slide 27: Poll #4
In addition to MALDI-ToF and BD-Phoenix, all of the following methods can help distinguish among Candida species except:
  A. Urea hydrolysis test
  B. Germ tube test
  C. Rice tween agar
  D. CHROMagar Candida
  E. Candida albicans screen test

## Slide 28: Poll #4
In addition to MALDI-ToF and BD-Phoenix, all of the following methods can help distinguish among Candida species except:
  A. Urea hydrolysis test
  B. Germ tube test
  C. Rice tween agar
  D. CHROMagar Candida
  E. Candida albicans screen test
Rapid screening test for Cryptococcus in respiratory specimens
Performed when Cryptococcus, Rhodotorula, Trichosporon species are suspected
  Cryptococcus and Rhodotorula are urease positive
  Trichosporon has both positive and negative species

## Slide 29: Germ Tube Test
Screening test for presumptive identification of C. albicans
Colony + reagent/serum for germ tube testing → incubated → wet mount
(+) Germ Tube Test | (-) Germ Tube Test
Short, slender, tube like structures arising laterally from yeast cell with NO constriction at point of origin | No hyphal extension arising from a yeast cell or a short hyphal extension with constriction at the point of origin
C. albicans [up to 5% clinical isolates germ tube (-)] C. dubliniensis | All other Candida spp C. tropicalis can produce pseudohyphae that closely resemble germ tubes
Notes: Minimum of 4 germ tubes should be observed before calling an organism positive
Growth at 45oC separates C. albicans from C. dubliniensis

## Slide 30: Rice Tween Agar
Morphology of yeast on Rice-Tween 80 Agar is a key characteristic used in yeast identification
Media enhances formation of hyphae and helps differentiation of yeasts, especially C. albicans, on the basis of chlamydospore formation
  C. albicans produces chlamydospores (terminal, round, thick walled) on corn meal/rice agar at 25oC
  C. dubliniensis also produces chlamydospores, but often multiple
Notes: If pseudohyphae and blastoconidia are present, a presumptive identification of Candida species can be made. The different patterns of growth in the cornmeal agar preparations are often sufficiently distinctive to establish presumptive species identification.
Chlamydospores are large terminal vesicles at the end of pseudohyphae

## Slide 31: CHROMagar
Selective and differential medium for the following Candida spp and C. auris
Other yeast species may develop either cream, or appear rose or light – dark mauve. For these, additional identification methods are needed
C. albicans Green - blue | C. krusei Pink with whitish border, fuzzy | C. tropicalis Metallic blue with pink halo | C. glabrata Mauve colonies*
Notes: Colonies of C. albicans, C. tropicalis, and C. krusei produce different colors, allowing for direct detection on agar plate

## Slide 32: C. albicans screen test
Identifies C. albicans by detection of enzymes L-proline aminopeptidase and B-galactosaminidase
C. albicans is positive for both enzymes, unlike other yeast species (except C. dubliniensis)
Presence of
B-galactosaminidase → yellow
Presence of
L-proline aminopeptidase → pink-red
Notes: Substrate for enzyme B-galactosaminidase on disc:
Positive: Yellow color
Negative: No yellow color
Substrate for enzyme L-proline aminopeptidase on disc:
Positive: pink – red color
Negative: no color change or slight yellow color

## Slide 33: Poll #5
24 year old man with HIV (CD4 55%/497, VL 28), Crohn’s disease complicated by perianal abscesses/fistulas on adalimumab. He was admitted for gastro-colonic fistula, inflammatory stricture of transverse colon causing obstruction and transverse colon intramural abscess and underwent ex-lap with right hemi-colectomy and gastric-colonic fistula take-down.
One week later he develops new fevers and leukocytosis. CT scan shows pneumoperitoneum concerning for leak, but repeat ex-lap notable for no perforation. He has a RUE PICC line that was placed 10 days ago. and is receiving enteral feeds through a G-J tube.
Bacterial blood cultures are positive by instrument after 20 hours of incubation

## Slide 34: Poll #5
Growth on Sabouraud agar
White, creamy, shiny Wrinkled or smooth colonies
Gram Stain (bacterial blood cultures)
Yeast forms with pseudohyphae
Yeast form
Pseudohyphae

## Slide 35: Poll #5
The organism identified in blood culture was most likely
A. Cryptococcus spp
B. Rhodotorula spp
C. Candida spp
D. Trichosporon spp
E. Malassezia furfur

## Slide 36: Poll #5
The organism identified in blood culture was most likely
A. Cryptococcus spp
B. Rhodotorula spp
C. Candida spp
D. Trichosporon spp
E. Malassezia furfur

## Slide 37: Poll #6
Additional studies:
Germ tube test: (-) | C. albicans screen test: (-)
Rice Tween agar: Short pseudohyphae (usually) with yeast in small groups or singularly at intervals along their length. No chlamydoconidia | CHROMagar: cream colored colonies

## Slide 38: Poll #6
The Candida spp identified in this patient’s blood culture was:
A. C. tropicalis
B. C. parapsilosis
C. C. albicans
D. C. glabrata
Germ tube test: (-) C. albicans screen test: (-) Rice Tween agar: Short pseudohyphae, no chlamydoconidia CHROMagar: cream colored colonies

## Slide 39: Poll #6
The Candida spp identified in this patient’s blood culture was:
A. C. tropicalis
B. C. parapsilosis
    C. C. albicans
    D. C. glabrata
Notes: C. tropicalis: negative germ tube test, negative CAS, no chlamydocondia, but blue/greenish – metallic blue on CHROMagar
C. albicans: (+) germ tube test, (+) CAS, chlamydocondia, green colonies on CHROMagar
C. glabrata:

## Slide 40: Poll #6
The Candida spp identified in this patient’s blood culture was:
A. C. tropicalis
B. C. parapsilosis
    C. C. albicans
D. C. glabrata
Usually appears as tiny budding yeast cells without pseudohyphae
Long pseudohyphae bearing yeast singly or in groups, occasional true hyphae
Pseudohyphae with large chlamydospores singly, occasionally multiple

## Slide 41: Poll #7
Which susceptibility pattern is most consistent with that of C. parapsilosis?
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. | S | R | S | S
2. | R | S | S | S
3. *no established breakpoints | +/- | R | +/- | +/-
4. | S | S | S | +/-
5. | S | R (usually) | S | S
**general patterns**

## Slide 42: Poll #7
Which susceptibility pattern is most consistent with that of C. parapsilosis?
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. | S | R | S | S
2. | R | S | S | S
3. *no established breakpoints | +/- | R | +/- | +/-
4. C. parapsilosis | S | S | S | +/-
5. | S | R (usually) | S | S
May have increased MIC to echinocandins

## Slide 43: Poll #8
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. | S | R | S | S
This Candida spp is most likely:
  C. krusei
  B. C. lusitaniae
  C. C. auris
  D. C. tropicalis

## Slide 44: Poll #8
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. C. krusei | S | R | S | S
Intrinsically resistant to fluconazole

## Slide 45: Poll #9
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. C. krusei | S | R | S | S
2. ? | R | S | S | S
This Candida spp is most likely:
  B. C. lusitaniae
  C. C. auris
  C. glabrata
  C. tropicalis

## Slide 46: Poll #9
 | Amphotericin B Formulations | Fluconazole | Voriconazole | Echinocandins
1. C. krusei | S | R | S | S
2. C. lusitaniae | R | S | S | S
Resistant to amphotericin
Other fungi resistant to amphotericin:
C. auris (some)
Aspergillus terreus
Scedosporium apiospermum (some)
Lometospora (Scedosporium) prolificans
Fusarium spp (some)
Sporothrix schenckii
Pseudallescheria boydii

## Slide 47: Summary
    Eswabs for fungal cultures, expect for superficial skin/mucous membranes specimens, are unacceptable. Sterile cup is specimen of choice.
    KOH-calcofluor preparation can help identify fungal elements to guide appropriate media and growth conditions. Lactophenol blue stain performed after fungal colony growth and helps identify morphological structures
    Communicate with the lab if a particular fungi is suspected to optimize media used and incubation conditions (e.g. Malassezia furfur requires fatty acids for growth; Mucormycosis; dimorphic fungi)
    C. albicans can be differentiated from other Candida spp using germ tube test (+), rice tween agar (chlamydocondia), CHROMagar, and Candida albicans screen
C. krusei → intrinsically resistant to fluconazole
C. lusitaniae → resistant to amphotericin
C. glabrata → usually fluconazole resistant (or SDD)
C. parapsilosis → occasional echinocandin resistance
C. auris → multi class resistance