| Animal Standard Operating Procedure Fluorine-18 (18F) |
| --- |
| Animal Safety Protocol designation | RS-1B Animal bedding and cages must be held for 10 half lives (19 hours) and surveyed before disposal. See investigator responsibilities below |
| Investigator Responsibility | Research staff must inform Animal Care staff ahead of time of agent that will be used, and arrangements will be made for isolation/quarantine housing of animals. Fresh micro-isolator caging will be used for the animals at the time of administration. Radiation Sign must be posted on the door of the room in which the animals will be housed while experiments are in progress. Cages will be labeled with a pink card with the following information: Name of agent delivered to animal Approximate dose Date of administration Date of bedding change Contact Information Animal husbandry performed by PI staff during period when isotope is present in animals until 10 half-lives. Cards and door signs must be removed by the researcher once the hazard is no longer present. Consult with the Radiation Safety Officer concerning shielding requirements. |
| Entry requirements | Access limited to PI staff and selected veterinary staff. All Personal Protective Equipment (PPE) gown, gloves, face mask, shoe covers and cap must be worn to enter animal room. Hands must be washed upon exiting animal room. Surgical mask, goggles, faceshield or use of a Biological Safety Cabinet (BSC) are required when conducting research. |
| Cage Change | Animal waste and contaminated bedding shall be handled to minimize generation of dust and aerosols. Radioactive bedding and cages will be held in “red bags” and labeled with the isotope and start date and anticipated decay date. Once 10 half-lives is reached, survey the bag to verify that waste has decayed and dispose in medical waste bin and transfer cages to IAS staff. |
| Decontamination and Spill Procedure | Once transferred to IAS, cages will be sanitized by standard IAS practices In the event of a radioactive spill, the area will be immediately restricted and cleaned and surveyed by laboratory personnel. Equipment and work surfaces must be routinely cleaned with 10% freshly prepared bleach or appropriate disinfectant. All equipment must be decontaminated prior to leaving the animal room. |